## Slide 1: FPGA Multi Effects Unit
Raymond Fleming
Digital Design
Fall 2018

## Slide 2: Guitar Effects
Distortion
  Overdrive
  Fuzz
Modulation
  Filter
  Wah
Time
  Chorus
  Delay/Echo

## Slide 3: Using the DE1-SoC
Code was used from Altera/Intel's tutorial lab 12
  Written mostly in Verilog
  Used to configure the Wolfson WM8731 24-bit CODEC.

## Slide 4: Block Diagram

## Slide 5: Noise Reduction
The input was found to be noisy. A 32-bit averaging filter was used to reduce noise.

## Slide 6: Volume
Volume/Boost effect
  Equivalent to a preamplifier.
  Output = Input * Multiplier

## Slide 7: Overdrive
Soft-Clipping Effect
  The top of the wave is squashed, rather than clipped.
  Output=cutoff-(input-cutoff)/2 for clipped section

## Slide 8: Fuzz
Hard-Clipping Effect
  Implemented by clipping the top off the input
  Output=4,000,000 if input > 4,000,000

## Slide 9: Octaver
Frequency Doubler Effect
  Modeled on analog octaver, which is a full wave rectifier.
  Output=Input when positive, -Input when negative

## Slide 10: Testing
The circuit was designed to use the slide switches for both volume input and to select the effects
The circuit was tested through a PC playing a clean guitar loop

## Slide 11: Further Effects
Time based effects could be added to the project with more time.
Reverb can be implemented using a large buffer, playing back signals after a delay with some signals played in reverse.
Chorus can be implemented by playing closely spaced samples mixed together, giving some constructive and destructive interference.

## Slide 12: Delay/Echo
Delay is similar to reverb, but with no reversed samples.
  With a longer delay, this is also an echo effect.

## Slide 13: Chorus
Chorus can be implemented using a smaller buffer, then playing back samples at closely spaced times.
  The times are given by a low frequency oscillator, effectively a counter.
  These samples provide constructive and destructive interference, giving a chorus sound.